## Slide 1
Where decontamination fits in oil & gas
OIL & GAS VALUE CHAIN
UPSTREAM
Production & gas processing
Oil production stations
Gas processing plants
Produced water & tank farms
MIDSTREAM
Transport & storage
Pipelines & pig receivers
Crude terminals & tank farms
LPG / NGL plants & spheres
DOWNSTREAM
Refining
Crude & vacuum units
Hydroprocessing & conversion
Sour water, amine & sulphur
PETROCHEMICALS
Chemicals & polymers
Aromatics (BTX)
Olefins & polymers
Methanol & fertilisers
✓ Every stage holds hydrocarbons, H₂S or pyrophoric scale – and needs decontamination before entry.
Notes: Build the value chain branch by branch. The green ticks mark where Delight decontaminates.

## Slide 2
Downstream – refining
OIL & GAS VALUE CHAIN
UPSTREAM
Production & gas processing
Oil production stations
Gas processing plants
Produced water & tank farms
MIDSTREAM
Transport & storage
Pipelines & pig receivers
Crude terminals & tank farms
LPG / NGL plants & spheres
DOWNSTREAM
Refining
PETROCHEMICALS
Chemicals & polymers
Aromatics (BTX)
Olefins & polymers
Methanol & fertilisers
Crude & vacuum units
Where: CDU, VDU, desalter, pre-heat trains
H₂S
Benzene
LEL
Heavy oil
Hydroprocessing & conversion
Where: Hydrotreaters, hydrocracker, FCC, coker
H₂S
Pyrophoric FeS
Coke
LEL
Sour water, amine & sulphur
Where: Sour water strippers, amine regenerators, SRU / TGT
H₂S
Ammonia
Pyrophoric FeS
Next: how vapour-phase decontamination clears these units.
Notes: Morph zooms into the Downstream branch: the tree shrinks to the corner and the refining leaves fly into the rows. Then the units and contaminants appear.

## Slide 3
Vapour-phase decontamination – how it works
To closed vent / flare
Column
H₂S
Benzene
LEL
FeS
GAS TEST AT MANWAY
LEL
✗ above limit
✓ OK
H₂S
✗ above limit
✓ OK
Benzene
✗ above limit
✓ OK
O₂
✗ above limit
✓ OK
STEAM
DECON CHEMISTRY
1 The unit is shut down, drained and isolated – but the column still holds toxic and flammable residues.
2 Steam is introduced through the existing steam-out lines and heats the whole column.
3 Decon chemistry is injected into the steam and travels to every surface the steam reaches.
4 H₂S, benzene and LEL gases are released and swept to the closed vent / flare; FeS is oxidised.
5 Deposits soften and drain – the column is clean.
6 Gas tests confirm the entry criteria – the column is handed over for safe entry.
✓ READY FOR SAFE ENTRY
Notes: Click through the six steps: steam, chemistry, contaminants swept out, column cleans, gas tests pass.