## Slide 1
DECONTAMINATION SERVICES
Safe, fast entry for BP Oman – Khazzan
Block 61, central Oman
Delight International · Maintenance Simplified
Notes: Introduce Delight and the purpose: a decontamination approach tailored to BP Oman – Khazzan & Ghazeer (Block 61).

## Slide 2
Agenda
01
Decontamination and your challenges
02
Application methods and chemistry
03
BP Oman – Khazzan units we decontaminate
04
Execution, monitoring and why Delight

## Slide 3
01
Decontamination and your challenges
What BP Oman – Khazzan needs before equipment is opened

## Slide 4: BP Oman – Khazzan: what has to be removed
FACILITY
Tight-gas central processing facility: inlet separation, gas dehydration, condensate stabilisation and compression.
Location Block 61, central Oman
KEY CONTAMINANTS
LEL (condensate)
BTEX / benzene
Pyrophoric FeS
Glycol residues
H₂S (where present)
Our focus: Gas-freeing condensate and dehydration equipment for planned shutdowns with verified entry conditions.
Notes: Site-specific contaminants and focus. Unit details are confirmed in a joint site survey.

## Slide 5: What is decontamination?
Decontamination prepares process equipment for safe entry and maintenance as quickly as possible – removing toxic and flammable gases, pyrophoric deposits and hydrocarbons before the equipment is opened.
Typical challenges at BP Oman – Khazzan: LEL (condensate), BTEX / benzene, Pyrophoric FeS, Glycol residues, H₂S (where present).
KEY ELEMENTS WE PLAN FOR
Method of application
Application time
Mechanical cleaning needs
Special requirements
Waste effluent quality

## Slide 6: Decontamination objectives
1
De-oiling / de-sludging
Soften heavy deposits for easier removal; reduce hazardous sludge and break up the rest.
2
Sulphide oxidation
Neutralise pyrophoric iron sulphide (FeS) and H₂S.
3
Degassing
Release flammable hydrocarbon gases (LEL), benzene and H₂S safely.
4
Neutralising
Correct pH and treat ammonia so effluent can be handled and disposed of.

## Slide 7: Simultaneous treatment in one application
Benzene
Below entry limit
LEL
Gas-free
H₂S & mercaptans
Below entry limit
Pyrophoric FeS
Neutralised
Heavy organics
Emulsified / removed
Residual solids
Conditioned
Distillation
Oxidation
Cleaning
Final entry criteria are agreed with the client and confirmed by gas testing before handover.

## Slide 8
02
Application methods and chemistry
Choosing the right method for each piece of equipment

## Slide 9: Application methods
Vapour-phase
Chemistry is carried by steam through existing steam-out lines
Minimal injection points
Fastest route to entry
Circulation
For specific vessels, exchangers and piping
Used where steam is not available
Boil-out
For vessels with large volumes of sludge
Water + steam + chemistry
Pre / post treatment
Oil wash / viscosity flush of heavy circuits
Tray and packing pre-treatment
Neutralising post-rinse

## Slide 10: Vapour-phase application
Column
Condenser
Reflux drum
H₂S
Benzene
Pyrophoric FeS
LEL
After optional pre-treatment, steam is introduced through the steam-out line.
Optional injection points: exchangers, heaters, strippers and drums.
STEAM
Notes: Steam is introduced first; the process vapour path is shown in light blue. Contaminants are released from the column internals.

## Slide 11: Vapour-phase application
Column
Condenser
Reflux drum
H₂S
Benzene
Pyrophoric FeS
LEL
STEAM
Once the overhead is steaming, decon chemistry is injected into the steam line.
The vapour-phase degreaser travels with the steam to every surface the steam reaches.
Injection continues until gas tests meet the entry criteria.
DECON CHEMISTRY
✓ Gas-free and pyrophoric-safe

## Slide 12: Boil-out application
Sludge
Water filled above the sludge level.
Steam injected at several points to heat the vessel.
Water-based solvent / degreaser added at temperature.
Boil-out continues until gas tests are met; vapours vented safely.
Add water
STEAM
STEAM
STEAM
CHEMISTRY
Vent
H₂S
Benzene
Pyrophoric FeS
LEL

## Slide 13: Circulation application – viscosity flush
Bottoms circuit
Exchanger
Unit shut down and de-inventoried under plant procedures.
Cutter stock / flushing oil circulated through the bottoms circuit and exchangers.
Oil-based solvent added to penetrate and break down heavy deposits.
OIL-BASED SOLVENT
H₂S
Benzene
Pyrophoric FeS
LEL

## Slide 14: Decontamination chemistry toolkit
Vapour-phase degreaser
Carried by steam; dissolves and lifts hydrocarbons; releases LEL and benzene for safe venting.
Use: Columns, overheads, exchangers
Water-based solvent
Emulsifies oil and sludge in water; non-flammable, low odour.
Use: Boil-out, circulation, tanks, rinses
Oil-based solvent
Boosts flushing oil to penetrate heavy deposits, tar and coke.
Use: Bottoms circuits, coker, quench oil
Sulphide / pyrophoric oxidiser
Converts pyrophoric iron sulphide and H₂S into safe compounds.
Use: Packed beds, amine, SWS, SRU
Neutraliser
Corrects pH and treats ammonia / acid residues for disposal.
Use: Post-rinse, effluent tanks
Antifoam / dispersant
Controls foaming and keeps solids dispersed.
Use: Amine systems, boil-outs
Chemistry is selected per unit after a compatibility check; product data and SDS are shared with the client.

## Slide 15
03
BP Oman – Khazzan units we decontaminate
Common challenges, chemistry and treatment options per unit

## Slide 16: Inlet Separation
Sludge / heavy deposits
Boot
COMMON CHALLENGES
Condensate and sludge
LEL
Large horizontal vessels
CHEMISTRY USED
Vapour-phase degreaser
Water-based solvent
TREATMENT OPTIONS
Boil-out
Vapour-phase
Indicative – confirmed during the joint site survey.

## Slide 17: Gas Dehydration
Reboiler / pump-around
Overhead drum
COMMON CHALLENGES
Glycol and BTEX residues
Hydrocarbon carry-over
CHEMISTRY USED
Vapour-phase degreaser
Water-based solvent
TREATMENT OPTIONS
Vapour-phase
Water-based rinse
Indicative – confirmed during the joint site survey.

## Slide 18: Condensate Stabilisation
Reboiler / pump-around
Overhead drum
COMMON CHALLENGES
LEL and benzene
FeS in reboilers
CHEMISTRY USED
Vapour-phase degreaser
Sulphide / pyrophoric oxidiser
TREATMENT OPTIONS
Vapour-phase
Indicative – confirmed during the joint site survey.

## Slide 19: Compression Scrubbers & KO Drums
Sludge / heavy deposits
Boot
COMMON CHALLENGES
Condensate and lube-oil residues
LEL
CHEMISTRY USED
Vapour-phase degreaser
Oil-based solvent
TREATMENT OPTIONS
Vapour-phase
Drum boil-out
Indicative – confirmed during the joint site survey.

## Slide 20: Condensate & Produced Water Tanks
Gamma-jet nozzle
Bottom sludge
COMMON CHALLENGES
Oil / sludge layers
LEL in vapour space
CHEMISTRY USED
Water-based solvent
TREATMENT OPTIONS
Gamma-jet circulation
Indicative – confirmed during the joint site survey.

## Slide 21
04
Execution, monitoring and why Delight
From site survey to handover

## Slide 22: How we execute
Site survey
P&IDs, isometrics, data sheets, injection points
Decon plan
Method statement, chemistry, volumes, waste plan
Mobilise & rig-up
Pumps, hoses, injection manifolds, effluent tanks
Decontaminate
Vapour-phase, circulation or boil-out with live monitoring
Validate & hand over
Gas tests against entry criteria, sign-off
Waste & demob
Neutralise, test and dispose via licensed contractor

## Slide 23: Division of responsibilities
DELIGHT
Decon engineering and method statement
Specialist supervisors and technicians
Decontamination chemistry
Pumps, injection hoses and manifolds
Gas monitoring during decontamination
Effluent neutralisation and waste coordination
BP OMAN – KHAZZAN
Isolation, de-inventory and permits
Steam, water, nitrogen and power utilities
Access to control room / DCS readings
Operators to drain low points
Laboratory support for sample analysis
Single point of contact

## Slide 24: Monitoring and validation
Multi-gas meter
LEL, H₂S, O₂ and CO at vents and manways
Benzene / VOC meter
PID readings and detector tubes for benzene
Gas sampling
Sample bombs to the client laboratory where required
Effluent checks
pH, COD and oil content before disposal
Decontamination is complete when the client’s entry criteria are met and confirmed by validation readings – then the equipment is handed over for opening.

## Slide 25: Less waste, less exposure
Less water than water washing
Vapour-phase uses steam already available on the unit.
Less confined-space entry
Equipment is gas-free and pyrophoric-safe before it is opened.
Controlled effluent
Collected in holding tanks, neutralised and tested before disposal.
Licensed disposal
Waste handled through approved contractors with full documentation.

## Slide 26: Why Delight
Certified QHSE
ISO 9001, ISO 14001 and ISO 45001 management system
Regional presence
UAE, Saudi Arabia, Oman, Qatar and India
Integrated services
Decontamination, chemical cleaning, hydro jetting, bundle extraction
Own fleet
HP / UHP units and 22 T – 65 T bundle extractors
Experienced crews
Trained supervisors and technicians for shutdown work
One point of responsibility
From survey and planning to waste handling and handover

## Slide 27
Thank you
Let’s plan the decontamination for your next BP Oman – Khazzan shutdown.
Delight Equipment International L.L.C.
P.O. Box 2932, Abu Dhabi, United Arab Emirates
Tel +971 2 5515641 · info@delightintl.ae · www.delightintl.ae
KSA (Jubail) +966 59348 1459 · India (Udupi) +91 9686433661