## Slide 1
Vapour-phase – where each contaminant goes
Column
FLARE /
CLOSED VENT
Condensate drain
EFFLUENT TANK
STEAM
DECON CHEMISTRY
GAS TEST AT MANWAY
LEL
✗ above limit
✓ OK
H₂S
✗ above limit
✓ OK
Benzene
✗ above limit
✓ OK
1 The unit is shut down, drained and isolated – the column still holds H₂S, benzene, LEL gases, pyrophoric FeS and heavy oil.
2 Steam is introduced through the existing steam-out lines and heats the whole column.
3 Decon chemistry is injected into the steam and reaches every surface the steam reaches.
4 H₂S is converted into stable, non-volatile compounds that stay in the condensate and drain to the effluent tank.
5 Pyrophoric FeS is oxidised in place to stable iron oxide – it can no longer self-heat – and is washed out.
6 Benzene and LEL hydrocarbons are vaporised and swept to the flare / closed vent; dissolved benzene drains with the condensate.
7 Softened deposits and heavy oil drain with the condensate – the column is clean.
8 Gas tests confirm the entry criteria – the column is handed over for safe entry.
H₂S
Benzene
LEL
FeS
stable salt
iron oxide
✓ READY FOR SAFE ENTRY
Notes: Eight clicks. H₂S and FeS are converted in place and leave with the condensate; only the vapours go to the flare.

## Slide 2
Boil-out – vessels with sludge
Vessel / drum
FLARE /
CLOSED VENT
STEAM
EFFLUENT TANK
Boiling
DECON CHEMISTRY
GAS TEST AT MANWAY
LEL
✗ above limit
✓ OK
H₂S
✗ above limit
✓ OK
Benzene
✗ above limit
✓ OK
1 The vessel is drained and isolated – sludge on the bottom, H₂S, benzene and LEL in the vapour space, pyrophoric FeS in the deposits.
2 Water is filled above the sludge level.
3 Steam is injected at several points along the bottom and brings the water to the boil.
4 Decon chemistry is added; the rolling boil lifts and emulsifies the sludge.
5 H₂S dissolves and is converted into stable compounds; FeS is oxidised to iron oxide – both stay in the water.
6 Benzene and LEL vapours leave through the vent to the flare / closed vent.
7 The vessel is drained to the effluent tank and rinsed – the vessel is clean.
8 Gas tests confirm the entry criteria – the vessel is handed over for safe entry.
H₂S
Benzene
LEL
FeS
stable salt
iron oxide
✓ READY FOR SAFE ENTRY
Notes: Eight clicks: fill, heat, chemistry and rolling boil, H₂S and FeS converted in the water, vapours to the flare, drain and rinse, gas test.