## Slide 1
DECONTAMINATION SERVICES
Safe, fast entry – across the oil & gas value chain
Delight International · Maintenance Simplified
Notes: Delight decontamination: where it is needed in oil & gas, how we do it, and what happens to every contaminant.

## Slide 2
Delight International at a glance
Regional presence
UAE, Saudi Arabia, Oman, Qatar and India
Certified QHSE
ISO 9001, ISO 14001 and ISO 45001
Sectors we serve
Onshore, offshore, marine, power and oil & gas
Integrated services
Plant maintenance, specialised services, flange management, pipeline, marine and tank cleaning
Decontamination at Delight: vapour-phase, boil-out, viscosity flush, chemical circulation, packing pre- & post-treatment and tank gamma-jet – planned, executed and validated by one team.

## Slide 3
Where decontamination fits in oil & gas
OIL & GAS VALUE CHAIN
UPSTREAM
Production & gas processing
Oil production stations
Gas processing plants
Produced water & tank farms
MIDSTREAM
Transport & storage
Pipelines & pig receivers
Crude terminals & tank farms
LPG / NGL plants & spheres
DOWNSTREAM
Refining
Crude & vacuum units
Hydroprocessing & conversion
Sour water, amine & sulphur
PETROCHEMICALS
Chemicals & polymers
Aromatics (BTX)
Olefins & polymers
Methanol & fertilisers
✓ Every stage holds hydrocarbons, H₂S or pyrophoric scale – and needs decontamination before entry.
Notes: Build the value chain branch by branch. The green ticks mark where Delight decontaminates. The next four slides zoom into each branch.

## Slide 4
Upstream – production & gas processing
OIL & GAS VALUE CHAIN
UPSTREAM
Production & gas processing
MIDSTREAM
Transport & storage
Pipelines & pig receivers
Crude terminals & tank farms
LPG / NGL plants & spheres
DOWNSTREAM
Refining
Crude & vacuum units
Hydroprocessing & conversion
Sour water, amine & sulphur
PETROCHEMICALS
Chemicals & polymers
Aromatics (BTX)
Olefins & polymers
Methanol & fertilisers
Oil production stations
Where: Separators, heater-treaters, desalters
H₂S
LEL
Sludge
FeS
Gas processing plants
Where: Slug catchers, amine, glycol, condensate stabilisers
H₂S
Mercaptans
FeS
Benzene
Produced water & tank farms
Where: Produced-water and condensate tanks
Sludge
H₂S
LEL
Notes: Morph zooms into upstream: the tree shrinks to the corner and the branch's facilities fly out. Click to show where we work and what is removed.

## Slide 5
Midstream – transport & storage
OIL & GAS VALUE CHAIN
UPSTREAM
Production & gas processing
Oil production stations
Gas processing plants
Produced water & tank farms
MIDSTREAM
Transport & storage
DOWNSTREAM
Refining
Crude & vacuum units
Hydroprocessing & conversion
Sour water, amine & sulphur
PETROCHEMICALS
Chemicals & polymers
Aromatics (BTX)
Olefins & polymers
Methanol & fertilisers
Pipelines & pig receivers
Where: Pig traps, receivers and slug catchers
FeS
Pigging debris
LEL
Crude terminals & tank farms
Where: Crude and product storage tanks
Sludge
Benzene
LEL
H₂S
LPG / NGL plants & spheres
Where: Fractionation columns, LPG spheres and bullets
LEL
Mercaptans
FeS
Notes: Morph zooms into midstream: the tree shrinks to the corner and the branch's facilities fly out. Click to show where we work and what is removed.

## Slide 6
Downstream – refining
OIL & GAS VALUE CHAIN
UPSTREAM
Production & gas processing
Oil production stations
Gas processing plants
Produced water & tank farms
MIDSTREAM
Transport & storage
Pipelines & pig receivers
Crude terminals & tank farms
LPG / NGL plants & spheres
DOWNSTREAM
Refining
PETROCHEMICALS
Chemicals & polymers
Aromatics (BTX)
Olefins & polymers
Methanol & fertilisers
Crude & vacuum units
Where: CDU, VDU, desalter, pre-heat trains
H₂S
Benzene
LEL
Heavy oil
Hydroprocessing & conversion
Where: Hydrotreaters, hydrocracker, FCC, coker
H₂S
FeS
Coke
LEL
Sour water, amine & sulphur
Where: Sour water strippers, amine regenerators, SRU / TGT
H₂S
Ammonia
FeS
Notes: Morph zooms into downstream: the tree shrinks to the corner and the branch's facilities fly out. Click to show where we work and what is removed.

## Slide 7
Petrochemicals – chemicals & polymers
OIL & GAS VALUE CHAIN
UPSTREAM
Production & gas processing
Oil production stations
Gas processing plants
Produced water & tank farms
MIDSTREAM
Transport & storage
Pipelines & pig receivers
Crude terminals & tank farms
LPG / NGL plants & spheres
DOWNSTREAM
Refining
Crude & vacuum units
Hydroprocessing & conversion
Sour water, amine & sulphur
PETROCHEMICALS
Chemicals & polymers
Aromatics (BTX)
Where: Reformer, extraction and xylene columns, aromatics tanks
Benzene
LEL
Heavy aromatics
Olefins & polymers
Where: Quench towers, caustic tower, compressor KO drums
Tar / coke
Polymer
Benzene
Methanol & fertilisers
Where: Desulphurisation, synthesis, distillation, ammonia sections
LEL
Ammonia
FeS
Notes: Morph zooms into petrochemicals: the tree shrinks to the corner and the branch's facilities fly out. Click to show where we work and what is removed.

## Slide 8
Your facility
FACILITY / CLIENT
UNITS IN SCOPE
KEY CONTAMINANTS
SHUTDOWN WINDOW
UTILITIES AVAILABLE (STEAM, N₂, WATER)
ENTRY CRITERIA / PERMIT REQUIREMENTS
Filled in with the client before the meeting – their position on the value chain and what we will remove.
Notes: Fill in this slide for each client meeting (type into the grey boxes).

## Slide 9
What has to be removed – and why
H₂S
Toxic gas – fatal at low concentrations
Benzene
Carcinogenic vapour – strict exposure limits
LEL hydrocarbons
Flammable / explosive atmosphere
Pyrophoric FeS
Self-heats and ignites when exposed to air
Heavy oil & sludge
Holds gases, blocks inspection, slows mechanical cleaning
Ammonia & mercaptans
Toxic and odorous – sour-water and LPG units
Notes: The hazards that must be removed before entry – the colours are used for these contaminants throughout the deck.

## Slide 10
Decontamination objectives
1
De-oiling / de-sludging
Soften heavy deposits for easier removal; reduce hazardous sludge.
2
Sulphide oxidation
Convert pyrophoric FeS and H₂S into stable, safe compounds.
3
Degassing
Release LEL hydrocarbons and benzene to the flare / closed vent.
4
Neutralising
Correct pH and treat ammonia so the effluent can be disposed of.

## Slide 11
01
How we decontaminate
Six methods – each shown with where every contaminant goes

## Slide 12
Which method, where?
Vapour-phase
Boil-out
Viscosity flush
Circulation
Pre/post-treat
Gamma-jet
Columns & towers
Drums, separators & desalters
Heavy bottoms, coker & quench oil
Exchangers & air coolers
Packed beds & trays
Tanks & temperature-limited vessels
● main method ○ used in combination / where applicable
Notes: The method is chosen per piece of equipment; most units combine two methods.

## Slide 13
Vapour-phase – where each contaminant goes
Column
FLARE /
CLOSED VENT
Condensate drain
EFFLUENT TANK
STEAM
DECON CHEMISTRY
GAS TEST AT VENTS / SAMPLE POINT
LEL
✗ above limit
↓ decreasing
✓ OK
H₂S
✗ above limit
↓ decreasing
✓ OK
Benzene
✗ above limit
↓ decreasing
✓ OK
Overhead condenser
Reflux drum
Reboiler
1 The unit is shut down, drained and isolated – the column still holds H₂S, benzene, LEL gases, pyrophoric FeS and heavy oil.
2 Steam is introduced through the existing steam-out lines and heats the whole column.
3 Decon chemistry is injected into the steam and reaches every surface the steam reaches.
4 H₂S is converted into stable, non-volatile compounds that stay in the condensate and drain to the effluent tank.
5 Pyrophoric FeS is oxidised in place to stable iron oxide – it can no longer self-heat – and is washed out.
6 Benzene and LEL hydrocarbons are swept to the flare / closed vent; dissolved benzene drains with the condensate.
7 Softened deposits and heavy oil drain with the condensate – the column is clean.
8 Gas tests confirm the entry criteria – the column is handed over for safe entry.
H₂S
Benzene
LEL
FeS
stable salt
iron oxide
✓ READY FOR SAFE ENTRY
Notes: Eight clicks. H₂S and FeS are converted in place and leave with the condensate; only the vapours go to the flare. The column cleans in stages from oily brown to Delight blue.

## Slide 14
Boil-out – vessels with sludge
Vessel / drum
FLARE /
CLOSED VENT
STEAM
DECON CHEMISTRY
EFFLUENT TANK
Boiling
GAS TEST AT VENTS / SAMPLE POINT
LEL
✗ above limit
↓ decreasing
✓ OK
H₂S
✗ above limit
↓ decreasing
✓ OK
Benzene
✗ above limit
↓ decreasing
✓ OK
1 The vessel is drained and isolated – sludge on the bottom, H₂S, benzene and LEL above it, pyrophoric FeS in the deposits.
2 Water is filled above the sludge level.
3 Steam is injected at several points along the bottom and brings the water to the boil.
4 Decon chemistry is injected with the steam; the rolling boil lifts and emulsifies the sludge.
5 H₂S dissolves and is converted into stable compounds; FeS is oxidised to iron oxide – both stay in the water.
6 Benzene and LEL vapours leave through the vent to the flare / closed vent.
7 The vessel is drained to the effluent tank and rinsed – the vessel is clean.
8 Gas tests confirm the entry criteria – the vessel is handed over for safe entry.
H₂S
Benzene
LEL
FeS
stable salt
iron oxide
✓ READY FOR SAFE ENTRY
Notes: Chemistry goes in with the steam through the bottom risers. The vessel cleans in stages from oily brown to Delight blue.

## Slide 15
Viscosity flush / oil wash – heavy deposits
Column bottoms
Exchanger
Pump
Flushing oil / cutter stock
OIL-BASED SOLVENT
SLOP / RERUN TANK
SAMPLE – RETURNING OIL
Clean flushing oil
Dark – picking up deposits
Lighter with each pass
Clear – flush complete
Overhead condenser
Reflux drum
FLARE / CLOSED VENT
Reboiler
1 Heavy bottoms, coker and quench circuits hold tar-like deposits that steam alone cannot shift.
2 Hot flushing oil (cutter stock) fills the bottoms circuit: column → pump → exchangers → column.
3 The oil circulates continuously through the circuit.
4 Oil-based solvent is added – it penetrates and softens the heavy deposits; the returning oil turns dark.
5 Pass after pass the deposits dissolve – the exchanger and column clean up and the sample gets lighter.
6 The loaded oil is sent to the slop / rerun tank – not to effluent.
7 Circuit clean – followed by vapour-phase for final gas-freeing.
NEXT: VAPOUR-PHASE GAS-FREEING
Notes: The returning-oil sample is how the end point is judged on site. Loaded oil goes to slop / rerun, then vapour-phase gas-frees the circuit.

## Slide 16
Chemical circulation – tanks & heat-limited vessels
Horizontal vessel – temperature-limited
No steam: lined, coated or low design temperature
to flare / closed vent
Mixing tank
Pump skid
RETURN-LINE MONITORING
H₂S
High
Decreasing ↓
Low ✓
pH
Off-spec
Neutral ✓
Iron (Fe)
Rising
Stable ✓
Gas test
Above limit
Decreasing ↓
OK ✓
EFFLUENT TANK
1 Temperature-limited vessels (lined, coated, low design temperature) cannot be steamed.
2 A temporary circulation skid is set up: mixing tank and pump, hosed to the equipment.
3 Decon solution is circulated continuously through the equipment and back to the mixing tank.
4 H₂S is converted into stable compounds and FeS is oxidised; LEL / benzene vapours are vented to the flare.
5 The return line is monitored until H₂S is low, pH is neutral and the iron level is stable.
6 The solution is drained to the effluent tank and a neutralising rinse follows.
7 Gas tests confirm the entry criteria – safe entry.
H₂S
Benzene
FeS
stable salt
iron oxide
✓ READY FOR SAFE ENTRY
Notes: Used where steam is not allowed: tanks and lined / coated / low-design-temperature vessels.

## Slide 17
Packing pre- & post-treatment – packed columns
1 PRE-TREATMENT
1 PRE-TREATMENT
2 VAPOUR-PHASE
2 VAPOUR-PHASE
3 POST-TREATMENT
3 POST-TREATMENT
Packed column
PRE-TREAT CHEMISTRY
OXIDISER SOLUTION
STEAM
FLARE /
CLOSED VENT
Packing pre-wetted
Packing pre-wetted
Packing pre-wetted
Benzene
LEL
FeS → iron oxide
FeS → iron oxide
FeS → iron oxide
!
Pyrophoric FeS left on the packing – ignites in air
EFFLUENT TANK
GAS TEST AT MANWAY
LEL
✗ above limit
↓ decreasing
✓ OK
H₂S
✗ above limit
↓ decreasing
✓ OK
Benzene
✗ above limit
↓ decreasing
✓ OK
Overhead condenser
Reflux drum
Reboiler
1 Packed beds hold hydrocarbon film and pyrophoric iron sulphide deep inside the packing geometry.
2 PRE-TREATMENT: decon chemistry is fed from the top and coats every surface of the packing.
3 With the packing pre-wetted, the vapour-phase that follows reaches deep into every bed.
4 VAPOUR-PHASE: steam carries the chemistry up through the beds – LEL and benzene go to flare.
5 Pyrophoric FeS can remain on the packing – it would self-heat once the column is opened.
6 POST-TREATMENT: an oxidiser wash trickles through each bed – FeS becomes stable iron oxide.
7 The spent wash drains to the effluent tank.
8 Gas tests pass – the column is safe to open and the packing safe to unload.
✓ SAFE TO OPEN & UNLOAD
Notes: Pre-treatment and post-treatment use the same circulation/spray route. Pre-treatment coats the packing geometry so the vapour-phase works deeper; post-treatment is the oxidation wash for pyrophoric FeS before opening.

## Slide 18
Tank decontamination – gamma-jet circulation
Storage tank
Gamma-jet nozzle
CARBON FILTER
treated vent
Vacuum pump
SLUDGE → DISPOSAL
Circulation pump
Recirculated wash water + chemistry
DECON CHEMISTRY
EFFLUENT TANK
GAS TEST AT VENTS / SAMPLE POINT
LEL
✗ above limit
↓ decreasing
✓ OK
H₂S
✗ above limit
↓ decreasing
✓ OK
Benzene
✗ above limit
↓ decreasing
✓ OK
1 Crude and product tanks: bottom sludge, and benzene, LEL and H₂S in the vapour space – entry is not allowed.
2 The tank vent is routed through a carbon filter – vapours are treated before release.
3 Bulk sludge is removed first: a vacuum pump transfers it to a waste tank for licensed disposal.
4 A gamma-jet nozzle is lowered through the roof manway; wash water with decon chemistry is circulated to it.
5 Gamma-jetting and circulation run for 8–12 hours – the jets sweep shell, roof and floor.
6 H₂S is converted into stable compounds; benzene and LEL vapours leave through the carbon filter.
7 Walls and floor are clean – the spent wash is drained to the effluent tank.
8 Gas tests confirm the entry criteria – safe entry.
H₂S
Benzene
LEL
stable salt
✓ READY FOR SAFE ENTRY
Notes: Tanks are atmospheric: no flare. Vapours are vented through a carbon filter. Bulk sludge is vacuumed to a waste tank for licensed disposal (no oil recovery), then gamma-jetting and circulation run for 8–12 hours; spent wash goes to the effluent tank.

## Slide 19
Where does each contaminant go?
Flare / closed vent
Vapours swept out with the steam or vented
Converted & drained
Made stable in the equipment, then drained to the effluent tank
Recovered oil
Heavy oil to the slop / rerun tank
Benzene
LEL
H₂S
FeS
Ammonia
Mercaptans
Sludge
Heavy oil
H₂S → stable salt
FeS → iron oxide
NH₃ → neutralised
Mercaptans → converted
Sludge → emulsified
Heavy oil → slop / rerun
Notes: Click 1: vapours to the flare. Click 2: H₂S, FeS, ammonia, mercaptans and sludge are converted / emulsified and drained. Click 3: heavy oil is recovered.

## Slide 20
Decontamination chemistry toolkit
Vapour-phase degreaser
Carried by steam; lifts hydrocarbons and releases LEL / benzene for safe venting.
Use: Columns, overheads, exchangers
Water-based solvent
Emulsifies oil and sludge in water; non-flammable, low odour.
Use: Boil-out, circulation, tanks
Oil-based solvent
Boosts flushing oil to penetrate heavy deposits, tar and coke.
Use: Viscosity flush, coker, quench oil
Sulphide / pyrophoric oxidiser
Converts H₂S and pyrophoric FeS into stable compounds.
Use: Post-treatment wash, packed beds, SWS, SRU
Neutraliser
Corrects pH and treats ammonia / acid residues for disposal.
Use: Post-rinse, effluent tanks
Antifoam / dispersant
Controls foaming and keeps solids dispersed.
Use: Amine systems, boil-outs
Chemistry is selected per unit after a compatibility check; product data and SDS are shared with the client.

## Slide 21
02
Execution and why Delight
From site survey to handover

## Slide 22
How we execute
Site survey
P&IDs, isometrics, data sheets, injection points
Decon plan
Method statement, chemistry, volumes, waste plan
Mobilise & rig-up
Pumps, hoses, injection manifolds, effluent tanks
Decontaminate
Vapour-phase, boil-out, flush or circulation with live monitoring
Validate & hand over
Gas tests against entry criteria, sign-off
Waste & demob
Neutralise, test and dispose via licensed contractor

## Slide 23
Division of responsibilities
DELIGHT
Decon engineering and method statement
Specialist supervisors and technicians
Decontamination chemistry
Pumps, skids, injection hoses and manifolds
Gas monitoring during decontamination
Effluent neutralisation and waste coordination
CLIENT
Isolation, de-inventory and permits
Steam, water, nitrogen and power utilities
Access to control room / DCS readings
Operators to drain low points
Laboratory support for sample analysis
Single point of contact

## Slide 24
Monitoring and validation
Multi-gas meter
LEL, H₂S, O₂ and CO at vents and manways
Benzene / VOC meter
PID readings and detector tubes for benzene
Gas sampling
Sample bombs to the client laboratory where required
Effluent checks
pH, COD and oil content before disposal
Decontamination is complete when the client’s entry criteria are met and confirmed by validation readings – then the equipment is handed over for opening.

## Slide 25
Less waste, less exposure
Less water than water washing
Vapour-phase uses steam already available on the unit.
Less confined-space entry
Equipment is gas-free and pyrophoric-safe before it is opened.
Controlled effluent
Collected in holding tanks, neutralised and tested before disposal.
Oil recovered, not wasted
Flushing oil goes back to slop / rerun.

## Slide 26
Why Delight
Certified QHSE
ISO 9001, ISO 14001 and ISO 45001 management system
Regional presence
UAE, Saudi Arabia, Oman, Qatar and India
Integrated services
Decontamination, chemical cleaning, hydro jetting, bundle extraction
Own fleet
HP / UHP units and 22 T – 65 T bundle extractors
Experienced crews
Trained supervisors and technicians for shutdown work
One point of responsibility
From survey and planning to waste handling and handover

## Slide 27
Thank you
Let’s plan the decontamination for your next shutdown.
Delight Equipment International L.L.C.
P.O. Box 2932, Abu Dhabi, United Arab Emirates
Tel +971 2 5515641 · info@delightintl.ae · www.delightintl.ae
KSA (Jubail) +966 59348 1459 · India (Udupi) +91 9686433661