## Slide 1
DECONTAMINATION SERVICES
Safe, fast entry for OQ Mina Al Fahal Refinery
Mina Al Fahal, Muscat
Delight International · Maintenance Simplified
Notes: Introduce Delight and the purpose: a decontamination approach tailored to OQ – Mina Al Fahal Refinery.

## Slide 2
Agenda
01
Decontamination and your challenges
02
Application methods and chemistry
03
OQ Mina Al Fahal Refinery units we decontaminate
04
Execution, monitoring and why Delight

## Slide 3
01
Decontamination and your challenges
What OQ Mina Al Fahal Refinery needs before equipment is opened

## Slide 4: OQ Mina Al Fahal Refinery: what has to be removed
FACILITY
Coastal refinery and crude export terminal with crude distillation, hydrotreating and reforming.
Location Mina Al Fahal, Muscat
KEY CONTAMINANTS
H₂S
Benzene
LEL (hydrocarbons)
Pyrophoric FeS
Heavy oil & sludge
Ammonia
Our focus: Short-window decontamination of process units and tankage close to a city – low emissions and minimal waste.
Notes: Site-specific contaminants and focus. Unit details are confirmed in a joint site survey.

## Slide 5: What is decontamination?
Decontamination prepares process equipment for safe entry and maintenance as quickly as possible – removing toxic and flammable gases, pyrophoric deposits and hydrocarbons before the equipment is opened.
Typical challenges at OQ Mina Al Fahal Refinery: H₂S, Benzene, LEL (hydrocarbons), Pyrophoric FeS, Heavy oil & sludge.
KEY ELEMENTS WE PLAN FOR
Method of application
Application time
Mechanical cleaning needs
Special requirements
Waste effluent quality

## Slide 6: Decontamination objectives
1
De-oiling / de-sludging
Soften heavy deposits for easier removal; reduce hazardous sludge and break up the rest.
2
Sulphide oxidation
Neutralise pyrophoric iron sulphide (FeS) and H₂S.
3
Degassing
Release flammable hydrocarbon gases (LEL), benzene and H₂S safely.
4
Neutralising
Correct pH and treat ammonia so effluent can be handled and disposed of.

## Slide 7: Simultaneous treatment in one application
Benzene
Below entry limit
LEL
Gas-free
H₂S & mercaptans
Below entry limit
Pyrophoric FeS
Neutralised
Heavy organics
Emulsified / removed
Residual solids
Conditioned
Distillation
Oxidation
Cleaning
Final entry criteria are agreed with the client and confirmed by gas testing before handover.

## Slide 8
02
Application methods and chemistry
Choosing the right method for each piece of equipment

## Slide 9: Application methods
Vapour-phase
Chemistry is carried by steam through existing steam-out lines
Minimal injection points
Fastest route to entry
Circulation
For specific vessels, exchangers and piping
Used where steam is not available
Boil-out
For vessels with large volumes of sludge
Water + steam + chemistry
Pre / post treatment
Oil wash / viscosity flush of heavy circuits
Tray and packing pre-treatment
Neutralising post-rinse

## Slide 10: Vapour-phase application
Column
Condenser
Reflux drum
H₂S
Benzene
Pyrophoric FeS
LEL
After optional pre-treatment, steam is introduced through the steam-out line.
Optional injection points: exchangers, heaters, strippers and drums.
STEAM
Notes: Steam is introduced first; the process vapour path is shown in light blue. Contaminants are released from the column internals.

## Slide 11: Vapour-phase application
Column
Condenser
Reflux drum
H₂S
Benzene
Pyrophoric FeS
LEL
STEAM
Once the overhead is steaming, decon chemistry is injected into the steam line.
The vapour-phase degreaser travels with the steam to every surface the steam reaches.
Injection continues until gas tests meet the entry criteria.
DECON CHEMISTRY
✓ Gas-free and pyrophoric-safe

## Slide 12: Boil-out application
Sludge
Water filled above the sludge level.
Steam injected at several points to heat the vessel.
Water-based solvent / degreaser added at temperature.
Boil-out continues until gas tests are met; vapours vented safely.
Add water
STEAM
STEAM
STEAM
CHEMISTRY
Vent
H₂S
Benzene
Pyrophoric FeS
LEL

## Slide 13: Circulation application – viscosity flush
Bottoms circuit
Exchanger
Unit shut down and de-inventoried under plant procedures.
Cutter stock / flushing oil circulated through the bottoms circuit and exchangers.
Oil-based solvent added to penetrate and break down heavy deposits.
OIL-BASED SOLVENT
H₂S
Benzene
Pyrophoric FeS
LEL

## Slide 14: Decontamination chemistry toolkit
Vapour-phase degreaser
Carried by steam; dissolves and lifts hydrocarbons; releases LEL and benzene for safe venting.
Use: Columns, overheads, exchangers
Water-based solvent
Emulsifies oil and sludge in water; non-flammable, low odour.
Use: Boil-out, circulation, tanks, rinses
Oil-based solvent
Boosts flushing oil to penetrate heavy deposits, tar and coke.
Use: Bottoms circuits, coker, quench oil
Sulphide / pyrophoric oxidiser
Converts pyrophoric iron sulphide and H₂S into safe compounds.
Use: Packed beds, amine, SWS, SRU
Neutraliser
Corrects pH and treats ammonia / acid residues for disposal.
Use: Post-rinse, effluent tanks
Antifoam / dispersant
Controls foaming and keeps solids dispersed.
Use: Amine systems, boil-outs
Chemistry is selected per unit after a compatibility check; product data and SDS are shared with the client.

## Slide 15
03
OQ Mina Al Fahal Refinery units we decontaminate
Common challenges, chemistry and treatment options per unit

## Slide 16: Crude Distillation Unit
Reboiler / pump-around
Overhead drum
COMMON CHALLENGES
Heavy fouling in bottoms
Steam distribution
Benzene / LEL in overheads
CHEMISTRY USED
Vapour-phase degreaser
Oil-based solvent
TREATMENT OPTIONS
Vapour-phase
Bottoms pre-flush
Indicative – confirmed during the joint site survey.

## Slide 17: Desalter
Sludge / heavy deposits
Boot
COMMON CHALLENGES
Sludge and emulsions
Contact and distribution
CHEMISTRY USED
Water-based solvent
Vapour-phase degreaser
TREATMENT OPTIONS
Boil-out
Indicative – confirmed during the joint site survey.

## Slide 18: Naphtha Hydrotreater & Reformer
Reactor
Effluent exchanger
Separator
COMMON CHALLENGES
Benzene-rich reformate
H₂S and FeS in the hydrotreater circuit
Chlorides in the reformer section
CHEMISTRY USED
Vapour-phase degreaser
Sulphide / pyrophoric oxidiser
Neutraliser
TREATMENT OPTIONS
Vapour-phase of strippers / stabiliser
Circulation of separators
Indicative – confirmed during the joint site survey.

## Slide 19: Kerosene & Gas Oil Treating
Sludge / heavy deposits
Boot
COMMON CHALLENGES
Mercaptans and caustic residues
Hydrocarbon LEL
CHEMISTRY USED
Vapour-phase degreaser
Neutraliser
TREATMENT OPTIONS
Vessel boil-out
Circulation
Indicative – confirmed during the joint site survey.

## Slide 20: Sour Water Stripper
Reboiler / pump-around
Overhead drum
COMMON CHALLENGES
H₂S and ammonia
FeS deposits
CHEMISTRY USED
Sulphide / pyrophoric oxidiser
Neutraliser
TREATMENT OPTIONS
Vapour-phase with oxidiser
Indicative – confirmed during the joint site survey.

## Slide 21: Crude & Product Tank Farm
Gamma-jet nozzle
Bottom sludge
COMMON CHALLENGES
Bottom sludge
Benzene / LEL in vapour space
Limited man-entry
CHEMISTRY USED
Water-based solvent
Vapour-phase degreaser
TREATMENT OPTIONS
Gamma-jet circulation
Heating where required
Indicative – confirmed during the joint site survey.

## Slide 22
04
Execution, monitoring and why Delight
From site survey to handover

## Slide 23: How we execute
Site survey
P&IDs, isometrics, data sheets, injection points
Decon plan
Method statement, chemistry, volumes, waste plan
Mobilise & rig-up
Pumps, hoses, injection manifolds, effluent tanks
Decontaminate
Vapour-phase, circulation or boil-out with live monitoring
Validate & hand over
Gas tests against entry criteria, sign-off
Waste & demob
Neutralise, test and dispose via licensed contractor

## Slide 24: Division of responsibilities
DELIGHT
Decon engineering and method statement
Specialist supervisors and technicians
Decontamination chemistry
Pumps, injection hoses and manifolds
Gas monitoring during decontamination
Effluent neutralisation and waste coordination
OQ MINA AL FAHAL REFINERY
Isolation, de-inventory and permits
Steam, water, nitrogen and power utilities
Access to control room / DCS readings
Operators to drain low points
Laboratory support for sample analysis
Single point of contact

## Slide 25: Monitoring and validation
Multi-gas meter
LEL, H₂S, O₂ and CO at vents and manways
Benzene / VOC meter
PID readings and detector tubes for benzene
Gas sampling
Sample bombs to the client laboratory where required
Effluent checks
pH, COD and oil content before disposal
Decontamination is complete when the client’s entry criteria are met and confirmed by validation readings – then the equipment is handed over for opening.

## Slide 26: Less waste, less exposure
Less water than water washing
Vapour-phase uses steam already available on the unit.
Less confined-space entry
Equipment is gas-free and pyrophoric-safe before it is opened.
Controlled effluent
Collected in holding tanks, neutralised and tested before disposal.
Licensed disposal
Waste handled through approved contractors with full documentation.

## Slide 27: Why Delight
Certified QHSE
ISO 9001, ISO 14001 and ISO 45001 management system
Regional presence
UAE, Saudi Arabia, Oman, Qatar and India
Integrated services
Decontamination, chemical cleaning, hydro jetting, bundle extraction
Own fleet
HP / UHP units and 22 T – 65 T bundle extractors
Experienced crews
Trained supervisors and technicians for shutdown work
One point of responsibility
From survey and planning to waste handling and handover

## Slide 28
Thank you
Let’s plan the decontamination for your next OQ Mina Al Fahal Refinery shutdown.
Delight Equipment International L.L.C.
P.O. Box 2932, Abu Dhabi, United Arab Emirates
Tel +971 2 5515641 · info@delightintl.ae · www.delightintl.ae
KSA (Jubail) +966 59348 1459 · India (Udupi) +91 9686433661